## Slide 1: Edge Detection
Chen-Kang (Angus) Tsai
Email: angus@cereal.cse.nsysu.edu.tw
Date: 2020/12/16

## Slide 2: Sobel Algorithm
Sobel algorithm is a kind of edge detection method
The purpose of edge detection is to identify the pixel value with significant change in brightness in digital images.
  It greatly reduce amount of data

## Slide 3: Sobel Operation
Sobel operation is to multiply input data with kernel
  Need to padding
The kernel has been fixed to two form
  X-direction
  Y-direction
255 | 255 | 255 | 235
135 | 234 | 54 | 56
0 | 12 | 43 | 43
0 | 121 | 121 | 12
-1 | 0 | 1
-2 | 0 | 2
-1 | 0 | 1
 | -119 |  | 
1 | 2 | 1
0 | 0 | 0
-1 | -2 | -1
 | 953 |  | 

## Slide 4: Sobel Operation
After the convolution operation, the next step is to give a threshold to determine where the edge is
  Threshold : 128
The lower the threshold, the more edges can be detected
High threshold will miss thin or short line segments

## Slide 5: Lab4
Software hardware co-design
System block
  clk
  reset
  Image
  Sobel
  Save

## Slide 6: Lab4
Image is used to read and store the pixel value
There are some signals to control the image block
  i_rd
  i_addr
0
1
2
65533
65534
65535
Pixel1
Pixel2
Pixel3
Pixel65534
Pixel65535
Pixel65536
Rom
Index
data

## Slide 7: Lab4
Write
  When output_valid changes to 1, the result is valid
  When all pixels are written, stop simulation.
    sc_stop()

## Slide 8: Lab4
Sobel
  You need to read the rom data cycle by cycle
  Reading data from ROM will delay one cycle
Sobel.h

## Slide 9: Lab4
Execution result
Original image
Direction Y
Direction X

## Slide 10: Platform Architect
Create project -> Project name -> Project file name -> OK

## Slide 11: Platform Architect
Import SystemC Modules -> Add -> Choose all the source file

## Slide 12: Platform Architect
Set the clk port of Image, Clock, Save and Sobel block to CLOCK protocol

## Slide 13: Platform Architect
Create the block diagram

## Slide 14: Platform Architect
Click clock block -> Set clock period
  division -> 5
  cycle -> 100000000
Click Reset block -> Set reset period
  _ticks -> 10

## Slide 15: Lab4
Execution result
Original image
Direction Y
Direction X

## Slide 16: Requirement
Due in one week (12/23)
  Complete Sobel operation.
  Use Platform Architecture to simulate output result.
  Source code ( all of your file, include PA project file, source code…. ).